## Slide 1
KPI & BSP Calculation Working Session
How we measure performance, and how we calculate the Best Shown Performance (BSP) benchmark
Folding Carton Actionable Intelligence Platform

## Slide 2
WORKING SESSION
Purpose of Today's Session
• Review exactly how each KPI and its BSP (Best Shown Performance) benchmark are calculated today — in plain business language, not code.
• Every formula shown was taken directly from the production calculation script — nothing here is invented.
• This is a working session, not a final declaration that the current methodology is correct.
Pilot Scope — keep in mind throughout
• Only 13 machines are currently in scope; all others are excluded.
• History is available from January 1, 2025 only — benchmarks are designed to use up to 24 months, but currently run on less than that.

## Slide 3
HOW IT WORKS
Overall Calculation Flow
Production / Event Data
KPI Calculation (per run)
Actual Performance (last week)
BSP / Target (from history)
BSP Performance (Actual vs BSP)
Sheet Gap (converted to sheets)
• Actual: what the machine did last week.
• BSP: the benchmark, built from that machine's own best demonstrated history.
• BSP Performance / Gap: the difference between Actual and BSP.
• Sheet Gap: that gap converted into an estimated number of sheets lost — the common scale used to rank every opportunity.

## Slide 4
THE CORE MECHANISM
How BSP Is Calculated
1
History pool: every qualifying run, ~last 24 months, run time > 2 hrs
2
Percentile, not best-ever: P75 (higher-better KPIs) or P25 (lower-better KPIs)
3
3 levels of specificity: Die (≥15 runs) → Board (≥25) → Machine (≥35)
4
Most specific level with enough data wins — sets HIGH / MEDIUM / LOW confidence
5
Die-level BSPs roll up to one machine-week BSP, weighted by scheduled hours
6
Coverage gate: insight only fires if >50% of the week's hours have a resolved BSP

## Slide 5
WORKED EXAMPLE
BSP Step-by-Step — Speed: Finding the Percentile
This machine + this specific die has 15 qualifying runs (RunHours > 2) over the lookback window. Each run's Speed (sheets produced ÷ run hours) is one data point in the pool.
Sorted low to high. Speed is a higher-is-better KPI, so BSP takes the 75th percentile — not the highest value (6,100), which could be a one-off. With 15 sorted values, the 75th percentile falls between the 11th value (5,500) and 12th value (5,600), interpolating to 5,550.
Result
BSP Speed (Level 1) = 5,550 sheets/hr
This is the speed the machine has already sustained across its own best quarter of runs — not its single fastest run.
Rank | Speed (sheets/hr)
1 | 4,800
2 | 4,850
3 | 4,900
4 | 5,000
5 | 5,050
6 | 5,100
7 | 5,150
8 | 5,200
9 | 5,300
10 | 5,400
11 | 5,500 ← P75 zone
12 | 5,600 ← P75 zone
13 | 5,700
14 | 5,900
15 | 6,100

## Slide 6
WORKED EXAMPLE
BSP Step-by-Step — Speed: Level Fallback & Sheet Gap
This week, Level 1 had exactly enough runs and resolved directly:
Level | Grain | Qualifying Runs | Minimum Needed | Resolved?
Level 1 — Die-specific | This machine + this exact die | 15 | 15 | Yes
Level 2 — Board-specific | This machine + board type/caliper | (not needed) | 25 | n/a
Level 3 — Machine-level | This machine, all products | (not needed) | 35 | n/a
Level 1 has exactly the 15 runs required, so it resolves — no fallback to Level 2 or Level 3 is needed this week. BSP Speed = 5,550 sheets/hr, confidence = HIGH.
If this die only had 9 qualifying runs instead of 15...
Level 1 — Die-specific: 9 runs vs. 15 needed → No — falls back | Level 2 — Board-specific: 31 runs vs. 25 needed → Yes — resolves here | Level 3 — Machine-level: 58 runs vs. 35 needed → (not needed)
BSP would instead come from Level 2 (this machine's board type/caliper pool, 31 runs) — a slightly broader comparison group, shown with MEDIUM confidence instead of HIGH, so the plant can see at a glance that the benchmark is less die-specific than usual.
Actual Speed = 5,200 sheets/hr, Run Hours = 90 → Sheet Gap = (5,550 − 5,200) × 90 = 31,500 sheets

## Slide 7
WHAT WE MEASURE
KPI Overview — 10 Published KPIs
KPI | Category | Direction
OEE | Outcome | Higher
Speed | Lever - OEE | Higher
Downtime % | Lever - OEE | Lower
Scrap Loss | Lever - OEE | Lower
Avg MR Time (Changeover / Makeready Time) | Lever - OEE | Lower
Avg Blanket Wash Time | Lever - Downtime % | Lower
Avg Feeder Trip Time | Lever - Downtime % | Lower
Blanket Washes per 10K | Lever - Downtime % | Lower
Feeder Trips per 10K | Lever - Downtime % | Lower
Downtime Reason (sub-reason breakdown) | Sub-lever of Downtime % | Lower

## Slide 8
OUTCOME
OEE — The Headline Number
Direction: Higher is better
The single headline number for how well the machine converted its scheduled time into good product, versus what it could have made running at its rated speed with zero downtime and zero scrap.
• Formula: OEE = Good Sheets Produced ÷ (Scheduled Hours × Rated Speed)
• BSP: BSP OEE is the 75th-percentile OEE achieved across the machine's own qualifying historical runs (Level 1 die-specific, falling back to Level 2 board-specific, then Level 3 machine-level — see BSP Calculation section).
• Sheet Gap: Sheet Gap = (BSP OEE − Actual OEE) × Scheduled Hours × Rated Speed
— Only time explicitly flagged as scheduled/crewed production time counts toward Scheduled Hours.
— Rated speed is machine-specific: Gluer and Window departments use their maximum recorded Gluer output rate; every other department uses OEM (nameplate
Worked Example
72.0% OEE
80.0% BSP OEE
Scheduled Hours = 120, Rated Speed = 6,000 sheets/hr
(0.80 − 0.72) × 120 × 6,000 = 57,600 sheets
≈ 57,600 sheets of lost output vs. this machine's own demonstrated best.

## Slide 9
LEVER
Speed
Direction: Higher is better
How fast the machine actually ran while producing, in sheets per run-hour.
• Formula: Speed = Total Sheets Produced (good + scrap) ÷ Run Hours
• BSP: 75th-percentile Speed from the same 3-level qualifying-run pool used for OEE.
• Sheet Gap: Sheet Gap = (BSP Speed − Actual Speed) × Run Hours
— Run hours counted only from scheduled/crewed time rows.
Worked Example
5,400 sheets/hr
6,000 sheets/hr BSP
Run Hours = 90
(6,000 − 5,400) × 90 = 54,000 sheets
≈ 54,000 sheets of output the machine could have produced running at its own demonstrated pace.

## Slide 10
LEVER
Downtime %
Direction: Lower is better
The share of scheduled time the machine was down (stopped) or in setup-down, rather than running.
• Formula: Downtime % = (Down Hours + Setup-Down Hours) ÷ Scheduled Hours
• BSP: 25th-percentile Downtime % from the same 3-level pool (a low downtime % is "good", so the bottom quartile is the benchmark).
• Sheet Gap: Sheet Gap = (Actual Downtime % − BSP Downtime %) × Scheduled Hours × BSP Speed
— Scheduled/crewed time only.
— Setup Down time is counted as downtime here, per the plant definition of downtime as (Time − Run) plus (Time − Setup), i.e. everything that is not pro
Worked Example
18.0% downtime
12.0% BSP downtime
Scheduled Hours = 120, BSP Speed = 6,000 sheets/hr
(0.18 − 0.12) × 120 × 6,000 = 43,200 sheets
≈ 43,200 sheets of lost capacity from excess downtime.

## Slide 11
SUB-LEVER
Downtime Reason Breakdown
Direction: Lower is better
Which specific named downtime reason codes (e.g. mechanical jam, material issue, quality check, etc. — excluding Blanket Wash / Feeder Trip / changeover reasons, which are their own KPIs above) are driving a machine's Downtime % problem. Up to the top 3 reasons by sheet impact are shown per machine per week.
• Formula: Reason Downtime % = Down Hours for that specific reason ÷ Total Scheduled Hours
• BSP: 25th-percentile of that specific reason's downtime rate, from a pool of qualifying runs that had that same reason recorded, resolved with the same Level 1 → 2 → 3 fallback as other KPIs (die-specific → board-sp...
• Sheet Gap: Sheet Gap = (Actual Reason Rate − BSP Reason Rate) × Total Scheduled Hours × BSP Speed
— Excludes MRO/changeover-coded reason rows (those belong to Avg MR Time).
— Excludes any reason code on the approved Blanket Wash / Feeder Trip list (those are their own dedicated KPIs above) — this prevents the same minutes o
— Reason rows with no reason code recorded are excluded.
Worked Example
6.0% of scheduled hours lost to "Mechanical Jam"
3.5% BSP for that same reason on that machine
Total Scheduled Hours = 120, BSP Speed = 6,000 sheets/hr
(0.06 − 0.035) × 120 × 6,000 = 18,000 sheets
≈ 18,000 sheets of lost output attributable specifically to Mechanical Jam.

## Slide 12
LEVER
Avg MR Time (Changeover Time)
Direction: Lower is better
The average time spent per changeover (makeready/setup) event.
• Formula: Avg MR Time = Total Setup Hours ÷ Number of Setup Events
• BSP: 25th-percentile setup hours-per-event from the qualifying pool, resolved at 3 levels the same way as other KPIs, but the pool is further split by MRO Class at every level, and by exact Material Description at L...
• Sheet Gap: Sheet Gap = (Actual Avg MR Time − BSP Avg MR Time) × Number of Setup Events × BSP Speed
— Only rows with at least one setup event count toward this KPI.
— The benchmark additionally distinguishes changeover complexity — a numeric MRO Class (1, 2, or 3) derived from the reason code — and, at the most spec
Worked Example
0.75 hr (45 min) average changeover
0.45 hr (27 min) BSP average changeover
Setup Events = 8, BSP Speed = 6,000 sheets/hr
(0.75 − 0.45) × 8 × 6,000 = 14,400 sheets
≈ 14,400 sheets of capacity lost to slower-than-demonstrated changeovers.

## Slide 13
LEVERS
Blanket Wash & Feeder Trip — Duration and Frequency
• Two events, each measured two ways: how long it takes (Avg Time) and how often it happens (per 10K sheets produced).
• Identified from an approved, exact list of reason-code descriptions — not a keyword search — to avoid false matches across plants.
• Excluded from the general Downtime Reason KPI so time is never counted twice.
KPI | Formula | BSP Pool
Avg Blanket Wash Time | Wash Hours ÷ Wash Events | Runs with ≥1 wash event
Avg Feeder Trip Time | Trip Hours ÷ Trip Events | Runs with ≥1 trip event
Blanket Washes per 10K | (Wash Events ÷ Total Sheets) × 10,000 | All qualifying runs, incl. 0-event runs
Feeder Trips per 10K | (Trip Events ÷ Total Sheets) × 10,000 | All qualifying runs, incl. 0-event runs

## Slide 14
SPECIAL BSP LOGIC
Scrap Loss → Expected Scrap → BSP Performance
Scrap does not use one flat target per machine — it uses an order-size-aware "expected scrap" benchmark instead.
Bucket order by size
P25 scrap % per bucket (6 mo.)
Expected = Bucket % × Order Sheets
Compare to Actual sheets scrapped
Worked Example
Machine runs one order in the "Mid" bucket (40,000 total sheets) this week.
This machine's 25th-percentile scrap rate for "Mid"-bucket orders, from its own last 6 months of single-setup orders, is 3.0%.
Expected Scrap = 3.0% × 40,000 = 1,200 sheets.
This order actually scrapped 1,600 sheets (4.0% of the order).
Scrap Loss = 1,600 − 1,200 = 400 sheets of excess scrap for this order.

## Slide 15
COMMON CURRENCY
Sheet Gap — Turning Every KPI Into Sheets
Sheet Gap is the platform's common currency for comparing very different kinds of shortfalls — a percentage-point gap in OEE, extra minutes per changeover, extra downtime events — on one scale: an estimated number of sheets the plant did not produce last week because performance on that KPI fell short of its own demonstrated BSP benchmark.
• No double-counting: OEE's own Sheet Gap is the machine's Total Sheet Impact; lever rows explain WHY, they are not added on top.
• Gated: Only counted when the gap is positive and BSP coverage exceeds 50%.
• Ranking: Opportunities within a plant are ranked by Sheet Impact, largest first.
• Streak is display-only: Consecutive-week or 4-week-above-BSP streaks are shown but do not change the Sheet Gap number.
Worked Example (OEE)
BSP OEE = 80%, Actual OEE = 72%
Scheduled Hours = 120, Rated Speed = 6,000 sheets/hr
Sheet Gap = (0.80 − 0.72) × 120 × 6,000 = 57,600 sheets
That 57,600-sheet OEE gap becomes the machine's Total Sheet Impact for the week on the summary report.

## Slide 16
GUARDRAILS
Key Filters & Exclusions
• Only scheduled/crewed time counts toward time-based KPIs; runs of 2 hours or less are excluded from every benchmark pool.
• Setup Down time counts as machine downtime (Downtime %), but is excluded from reason-level downtime — reason codes attribute only Down time.
• MRO/changeover reason codes and the approved Blanket Wash / Feeder Trip reason list are both excluded from the general Downtime Reason KPI, so nothing is counted twice.
• Scrap Loss (actual and benchmark) is restricted to single-setup orders only.
• Every insight requires BSP coverage strictly greater than 50% of the week's scheduled (or, for Scrap, sheet) volume before it is published.

## Slide 17
Plant Discussion
• Are these the right KPI definitions — are we measuring what we intend to measure?
• Are the right events included, and are the right events excluded?
• Are the current filters correct for your plant and machines?
• Is the BSP target (percentile + minimum pool size) reasonable and appropriately ambitious?
• Is the BSP performance / Sheet Gap comparison method fair?
• Should any KPI use different special logic (e.g. expected scrap)?
• Does Sheet Gap represent plant performance the way it should?
• See the full "Items for Plant Review" list in the reference document for 13 specific discussion points.